## Slide 1
The e-ASTROGAM gamma-ray space mission
A sensitive wide-field observatory
for the MeV / sub-GeV band
Vincent Tatischeff
On behalf of the e-ASTROGAM Collaboration

## Slide 2
e-ASTROGAM
The MeV/sub-GeV domain
Worst covered part of the electromagnetic spectrum (only a few tens of steady sources detected so far between 0.2 and 30 MeV)
Many objects have their peak emissivity in this range (GRBs, blazars, pulsars...)
2

## Slide 3
e-ASTROGAM
Observational challenges
Photon interaction probability reaches a minimum at ~ 10 MeV
Three competing processes of interaction, Compton scattering being dominant around 1 MeV  complicated event reconstruction
The MeV range is the domain of nuclear g-ray lines (radioactivity, nuclear collision, positron annihilation, neutron capture)
Strong instrumental background from activation of space-irradiated materials
3

## Slide 4
e-ASTROGAM
g-ray astronomy in context
4
Need for a sensitive, wide-field g-ray space observatory operating at the same time as facilities like SKA and CTA, as well as eLISA and neutrino detectors, to get a coherent picture of the transient sky and the sources of gravitational waves and high-energy neutrinos
?
New Astronomies: gravitational waves neutrinos
CTA
Athena
E-ELT
JWST
ALMA
SKA
eLISA - Gravitational waves
IceCube-Gen2 - Neutrinos

## Slide 5
e-ASTROGAM
Gamma-ray polarization
5
g-ray polarization in objects emitting jets (GRBs, Blazars, X-ray binaries) or with strong magnetic field (pulsars, magnetars)  magnetization and content (hadrons, leptons, Poynting flux) of the outflows + radiation processes
g-ray polarization from cosmological sources (GRBs, Blazars)  fundamental questions of physics related to Lorentz Invariance Violation (vacuum birefringence)
e-ASTROGAM will measure the g-ray polarization of ~ 100 GRBs per year (promising candidates for highly g-ray polarized sources)
DE = 0.2 - 1 MeV
P = (75.0 ± 7.2)%
GRB 140206A with e-ASTROGAM
INTEGRAL/IBIS - GRB 140206A (z = 2.74)
Qoff-axis = 30°
Götz et al. (2014)
P > 48% (68% c. l.)

## Slide 6
e-ASTROGAM
Cygnus region in the 1 - 3 MeV energy band with the e-ASTROGAM PSF (extrapolation of the 3FGL source spectra to low energies)
Angular resolution
6
Angular resolution needs to be improved close to the physical limits (Doppler broadening, nuclear recoil)
Notes: ASTROGAM angular resolution better than that of COMPTEL by a factor of 4 at 5 MeV and better than that of Fermi/LAT by a factor of 3.5 at 1 GeV.
ASTROGAM energy resolution is about 10 keV (1 sigma) at 1 MeV. Is a factor of 4 better than COMPTEL

## Slide 7
e-ASTROGAM
Tracker - Double sided Si strip detectors (DSSDs) for excellent spectral resolution and fine 3-D position resolution
Calorimeter - High-Z material for an efficient absorption of the scattered photon  CsI(Tl) scintillation crystals readout by Si Drift Diodes for better energy resolution
Anticoincidence detector to veto charged-particle induced background  plastic scintillators readout by Si photomultipliers
Measurement principle
Tracker
Calorimeter
7
g
Compton e-

## Slide 8
e-ASTROGAM
Detail of the detector-ASIC bonding in the AGILE Si Tracker
8
Payload
Fermi/LAT AC system
PICSiT CsI(Tl) pixel
Calorimeter: 33 856 CsI(Tl) bars coupled at both ends to low-noise Silicon Drift Detectors
ACD: segmented plastic scintillators coupled to SiPM by optical fibers
Heritage: AGILE, Fermi/LAT, AMS-02, INTEGRAL, LHC/ALICE…
Tracker: 56 layers of 4 times 5×5 DSSDs (5 600 in total) of 500 mm thickness and 240 mm pitch
DSSDs bonded strip to strip to form 5×5 ladders
Light and stiff mechanical structure
Ultra low-noise front end electronics

## Slide 9
e-ASTROGAM
Mission profile
Orbit - Equatorial (inclination i < 2.5°, eccentricity e < 0.01) low-Earth orbit (altitude in the range 550 - 600 km)
Launcher - Ariane 6.2
Satellite communication -
ESA ground station at Kourou
+ ASI Malindi station (Kenya)
Data transmission - via X-band (available downlink of 10 Mbps)
Observation modes - (i) zenith-pointing sky-scanning mode, (ii) nearly inertial pointing, and (iii) fast repointing to avoid the Earth in the field of view
In-orbit operation - 3 years duration + provisions for a 2+ year extension
Background environment in an ELEO
9

## Slide 10
e-ASTROGAM
Performance assessment
10
e-ASTROGAM performance evaluated with MEGAlib (Zoglauer et al. 2006) and Bogemms (Bulgarelli et al. 2012) - both tools based on Geant4 - and a detailed numerical mass model of the gamma-ray instrument

## Slide 11
e-ASTROGAM
Core science
11
Jet astrophysics: a unique link to new astronomies (gravitational waves, neutrinos, ultra-high energy cosmic rays)
The high-energy mysteries of the Galactic center region
Supernovae, nucleosynthesis and Galactic chemical evolution

## Slide 12
PKS 2149-306 (z = 2.345)
e-ASTROGAM
Launch of ultra-relativistic jets in GRBs? Ejecta composition, energy dissipation site, radiation processes?
Can short-duration GRBs be unequivocally associated to gravitational wave signals?
How does the accretion disk/jet transition occur around supermassive black holes in AGN?
Are BL Lac blazars sources of UHECRs and high-energy neutrinos?
12
Core science topic #1
Jet astrophysics in the era of new astronomies
With its wide field of view, unprecedented sensitivity over a large spectral band, and exceptional capacity for polarimetry, e-ASTROGAM will give access to a variety of extreme transient phenomena
e-ASTROGAM

## Slide 13
e-ASTROGAM
Fermi/LAT
E > 1.7 GeV
INTEGRAL/SPI - 511 keV (Bouchet et al. 2010)
INTEGRAL/SPI
e-ASTROGAM FWHM
13
Core science topic #2
The high-energy mysteries at the Galactic Center
Origin of the Fermi Bubbles and of the 511 keV emission from the Galaxy’s bulge? Are these linked to a past activity of the central supermassive black hole? What is causing the GeV excess emission from the center region?
With a sensitivity and an angular resolution in the MeV - GeV range significantly improved over previous missions, e-ASTROGAM will enable a detailed spectro-imaging of the various high-energy components

## Slide 14
e-ASTROGAM
Core science topic #3
14
Supernovae, nucleosynthesis, and Galactic chemical evolution
How do thermonuclear and core-collapse SNe explode? How are cosmic isotopes created in stars and distributed in the interstellar medium?
missions, e-ASTROGAM should allow us to finally understand the progenitor system(s) and explosion mechanism(s) of Type Ia SNe (56Ni, 56Co), the dynamics of core collapse in massive star explosions (56Co, 57Co), and the history of recent SNe in the Milky Way (44Ti, 60Fe...)
With a remarkable improvement in g-ray line sensitivity over previous
(adapted from Diehl et al. 2015)

## Slide 15
Solar System
Supermassive Black Holes
Radio Galaxies
Blazars
FSRQs
BL Lacs
Other/Unknown
Radio Lobes
Central Engine
Sgr A*
Unidentified
Solar Flares
Terrestrial g-Ray Flashes
Gamma-Ray Source Classes
Gamma-Ray Bursts
Short
Long
Milky Way
Superbubbles
Molecular Clouds
Star-forming Regions
Stellar Objects
Pulsars
>1000 sources expected with e-ASTROGAM
Magnetospheric emission
Pulsar Wind Nebulae
Starburst Galaxies
Binary Systems
Novae
Interstellar Medium
Supernovae
Core-collapse
Supernova Remnants
Thermonuclear
Globular Clusters
Satellite Galaxies
Magnetars
Black Hole Binaries
Neutron Star binaries
Colliding Winds
Galaxy’s Bulge

## Slide 16
e-ASTROGAM
Over 3/4 of the sources from the 3rd Fermi LAT Catalog (3FGL), 2415 sources over 3033, have power-law spectra (Eg > 100 MeV) steeper than Eg-2, implying that their peak energy output is below 100 MeV
These includes more than 1200 (candidate) blazars (mostly FSRQ), about 150 pulsars, and nearly 900 unassociated sources
Most of these sources will be detected by e-ASTROGAM  large discovery space for new sources and source classes
16
Discovery space
Notes: Flat Spectrum Radio Quasars = most distant and energetic LAT sources
Unassociated (unidentified) sources => large discovery space

## Slide 17
e-ASTROGAM
Collaboration
INFN, INAF, University Tor Vergata, University of Udine | 
CSNSM, IRAP, APC, CEA, LLR, LUPM, IPNO | 
Univ. Mainz, Univ. Wuerzburg, MPE, RWTH, DESY, Univ. Erlangen | 
ICE (CSIC-IEEC), IMB-CNM (CSIC), IFAE-BIST, Univ. Barcelona | 
University College Dublin, DIAS | 
DTU | 
University of Geneva | 
Jagiellonian University, CBK, NCAC | 
NASA GSFC, NRL, Clemson Univ., Washington Univ., Yale Univ., UC Berkeley | 
Ioffe Institute | 
University of Tokyo | 
Principal investigator: Alessandro De Angelis (INFN, Italy)

## Slide 18
e-ASTROGAM
The MeV / sub-GeV gamma-ray band is potentially one of the richest energy domain of astronomy
e-ASTROGAM will be an essential observatory to study the extreme transient sky at the era of astronomy’s new messengers
The e-ASTROGAM payload is innovative in many respects, but the technology is ready
18
Conclusions